## Slide 1
COMPUTER NETWORKS
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Computer Networks and the Internet
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 3
COMPUTER NETWORKS
Performance: Packet Queueing Delay revisited
Unlike other delays (dproc, dtrans, dprop), dqueue is interesting.
Can vary from packet to packet.
Characterize dqueue -> average, variance, probability that it exceeds some specified value.
When is the queuing delay large and when is it insignificant?
Rate at which traffic arrives at the queue,
Transmission rate of the link,
Nature of the arriving traffic – periodically or in bursts

## Slide 4
COMPUTER NETWORKS
Performance: Packet Queueing Delay revisited
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate (pps)
La: avg. rate at which bits arrive at the queue
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R <= 1: nature of arriving traffic
La/R ~ 0: avg. queueing delay small
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
Design your system so that the traffic intensity is no greater than 1.
La/R > 1: Average rate at which bits arrive at the queue exceeds the rate at which the bits can be transmitted from the queue.

## Slide 5
COMPUTER NETWORKS
“Real” Internet Delays and Routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 6
COMPUTER NETWORKS
“Real” Internet Delays and Routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic link
* Do some traceroutes from exotic countries at www.traceroute.org
looks like delays decrease! Why?
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu

## Slide 7
COMPUTER NETWORKS
Performance: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 8
COMPUTER NETWORKS
Performance: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 9
COMPUTER NETWORKS
Performance: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 10
COMPUTER NETWORKS
Performance: Throughput – Network Scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/
Suppose Rs = 2 Mbps, Rc = 1 Mbps, R = 5 Mbps
10 clients from 10 servers = 10 downloads
End-to-end throughput for each download is now reduced to 500 kbps.

## Slide 11
COMPUTER NETWORKS
Queries

## Slide 12
sivaramane@pes.edu
+91 80 6666 3333 Extn 834
THANK YOU
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering