## Slide 1
COMPUTER NETWORKS
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Application Layer
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 3
COMPUTER NETWORKS
  2.1 Principles of Network Applications
  2.2 Web, HTTP and HTTPS
  2.3 The Domain Name System
  2.4 P2P Applications
  2.5 Socket Programming with TCP & UDP
  2.6 Other Application Layer Protocols
Unit – 2 Application Layer

## Slide 4
COMPUTER NETWORKS
DNS name resolution: iterated query
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu
Iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server

## Slide 5
COMPUTER NETWORKS
DNS name resolution: recursive query
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu

## Slide 6
COMPUTER NETWORKS
Caching and Updating DNS Records
Suppose that a host apricot.nyu.edu queries dns.nyu.edu for the IP address for the hostname cnn.com. After an hour later, another NYU host, say, kiwi.nyu.edu, also queries dns.nyu.edu.
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best-effort name-to-address translation!)
  if name host changes IP address, may not be known Internet-wide until all TTLs expire!
update/notify mechanisms proposed IETF standard
  RFC 2136

## Slide 7
COMPUTER NETWORKS
DNS Records
DNS: distributed database storing resource records (RR)
type=NS
  name is domain (e.g., foo.com)
  value is hostname of authoritative name server for this domain
RR format: (name, value, type, ttl)
type=A
  name is hostname
  value is IP address
type=CNAME
  name is alias name for some “canonical” (the real) name
  www.ibm.com is really servereast.backup2.ibm.com
  value is canonical name
type=MX
  value is canonical name of a mailserver associated with alias hostname name
relayl.bar.foo.com, 145.37.93.126, A
foo.com, dns.foo.com, NS
ibm.com, servereast.backup2.ibm.com, CNAME
example.com, mail.example.com, MX

## Slide 8
COMPUTER NETWORKS
DNS Protocol Messages
DNS query and reply messages, both have same format:
message header:
identification: 16 bit # for query, reply to query uses same #
flags:
  query or reply (1-bit)
  recursion desired
  recursion available
  reply is authoritative
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
12 bytes
Name, type fields for
a query
RRs in response to query
Records for
authoritative servers
Additional “helpful”
info that may be used

## Slide 9
COMPUTER NETWORKS
DNS query and reply messages, both have same format:
identification
flags
# questions
questions (variable # of questions)
# additional RRs
# authority RRs
# answer RRs
answers (variable # of RRs)
authority (variable # of RRs)
additional info (variable # of RRs)
2 bytes
2 bytes
name, type fields for a query
RRs in response to query
records for authoritative servers
additional “ helpful” info that may be used
DNS Protocol Messages
Type (for example, A, NS, CNAME, and MX), the Value, and the TTL.

## Slide 10
COMPUTER NETWORKS
Emulating Local DNS Server (Step 1: Ask Root)
Directly send the query to this server.
No answer (the root does not know the answer)
Go ask them!

## Slide 11
COMPUTER NETWORKS
Steps 2-3: Ask .net & example.net servers
Ask a .net nameservers.
Ask an example.net nameservers.
Go ask them!
Finally got the answer

## Slide 12
COMPUTER NETWORKS
Summary

## Slide 13
COMPUTER NETWORKS
Inserting records into DNS
Example: new startup “Network Utopia”
register name networkuptopia.com at DNS registrar (e.g., Network Solutions)
  provide names, IP addresses of authoritative name server (primary and secondary)
  registrar inserts NS, A RRs into .com TLD server:
  (networkutopia.com, dns1.networkutopia.com, NS)
  (dns1.networkutopia.com, 212.212.212.1, A)
create authoritative server locally with IP address 212.212.212.1
  type A record for www.networkuptopia.com
  type MX record for networkutopia.com

## Slide 14
COMPUTER NETWORKS
DNS Request - Wireshark Packet Capture

## Slide 15
COMPUTER NETWORKS
DNS Response - Wireshark Packet Capture

## Slide 16
COMPUTER NETWORKS
Suggested Readings
DNS (Domain Name System) – Explained – https://youtu.be/JkEYOt08-rU
How a DNS Server (Domain Name System) works – https://youtu.be/rdVPflECed8
Wireshark Lab: DNS v7.0 – http://www-net.cs.umass.edu/wireshark-labs/Wireshark_DNS_v7.0.pdf

## Slide 17
sivaramane@pes.edu
+91 80 6666 3333 Extn 834
THANK YOU
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering