## Slide 1
COMPUTER NETWORKS
Animesh Giri
Department of Computer Science & Engineering

## Slide 2
COMPUTER NETWORKS
Transport Layer
Animesh Giri
Department of Computer Science & Engineering

## Slide 3
COMPUTER NETWORKS
TCP Congestion Control
Animesh Giri
Department of Computer Science & Engineering

## Slide 4: In this segment
COMPUTER NETWORKS
TCP congestion control: additive increase multiplicative decrease
TCP Congestion Control: details
TCP Slow Start
TCP: detecting, reacting to loss
TCP: switching from slow start to CA
Summary: TCP Congestion Control
TCP throughput
TCP Futures: TCP over “long, fat pipes”
TCP Fairness
Why is TCP fair?
Explicit Congestion Notification (ECN)

## Slide 5
TCP congestion control: additive increase multiplicative decrease
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
  multiplicative decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time
COMPUTER NETWORKS

## Slide 6
TCP Congestion Control: details
sender limits transmission:
cwnd is dynamic, function of perceived network congestion
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
cwnd
LastByteSent-
LastByteAcked
<
cwnd
sender sequence number space
rate
~
~
cwnd
RTT
bytes/sec
COMPUTER NETWORKS

## Slide 7
TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments
COMPUTER NETWORKS

## Slide 8
TCP: detecting, reacting to loss
loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold, then grows linearly
loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)
COMPUTER NETWORKS

## Slide 9
TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
COMPUTER NETWORKS

## Slide 10
Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!
COMPUTER NETWORKS

## Slide 11
TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec
COMPUTER NETWORKS

## Slide 12
TCP Futures: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L
COMPUTER NETWORKS

## Slide 13
TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2
COMPUTER NETWORKS

## Slide 14
Why is TCP fair?
two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
COMPUTER NETWORKS

## Slide 15
Fairness (more)
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2
COMPUTER NETWORKS

## Slide 16
Explicit Congestion Notification (ECN)
network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
congestion indication carried to receiving host
receiver (seeing congestion indication in IP datagram) ) sets ECE bit on receiver-to-sender ACK segment to notify sender of congestion
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
ECN=11
ECN=00
ECN=11
ECE=1
IP datagram
TCP ACK segment
COMPUTER NETWORKS

## Slide 17
animeshgiri@pes.edu
+91 80 6618 6603
THANK YOU
Animesh Giri
Department of Computer Science & Engineering