## Slide 1
COMPUTER NETWORKS
S Nagasundari
Department of Computer Science and Engineering

## Slide 2
Text Book
COMPUTER NETWORKS
Slides adapted from
Computer Networking: A Top-Down Approach Jim Kurose, Keith Ross Pearson, 2017, 8th Ed.
TCP/IP protocol suite , Behrouz A. Forouzan.,4th Ed.

## Slide 3
COMPUTER NETWORKS
Link Layer and LAN
S Nagasundari
Department of Computer Science and Engineering

## Slide 4
Introduction
Error detection, correction
Multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
Physical layer
Wireless LANs: IEEE 802.11
A day in the life of a web request
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 5
COMPUTER NETWORKS
Introduction to link layer
Error detection and correction techniques
  Parity Checks
  Internet Checksum
  Cyclic Redundancy Check
Class 47 : Intro to Link layer : Learning Objectives

## Slide 6
Introduction to Link layer
COMPUTER NETWORKS
link layer has responsibility of
transferring datagram from one node to physically adjacent node over a link
mobile network
enterprise
network
national or global ISP
datacenter
network
Terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired
  wireless
  LANs
layer-2 packet: frame, encapsulates datagram

## Slide 7
Datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
Each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy:
trip from Mysore to Jaipur
  Car: Mysore to Bangalore
  plane: Bangalore to Delhi
  train: Delhi to Jaipur
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm
Link layer : context
COMPUTER NETWORKS

## Slide 8
…
…
Link layer : services
COMPUTER NETWORKS
Framing:
  encapsulate datagram into frame, adding header, trailer
Link access:
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)

## Slide 9
…
…
Link layer : services
COMPUTER NETWORKS
Reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 10
Link layer : services (more)
COMPUTER NETWORKS
Flow control:
  pacing between adjacent sending and receiving nodes
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
…
…

## Slide 11
Link layer : services (more)
COMPUTER NETWORKS
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Half-duplex and Full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…

## Slide 12
In each-and-every host
Link layer implemented in network interface card (NIC) or on a chip
  Ethernet, WiFi card or chip
  implements link, physical layer
Attaches into host’s system buses
Combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
Where is the link layer implemented?
COMPUTER NETWORKS
application
transport
network
link
link
physical

## Slide 13
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
Sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
Receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram
Interfaces communicating
COMPUTER NETWORKS

## Slide 14
Introduction
Error detection, correction
Multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 15
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram
COMPUTER NETWORKS
Error detection

## Slide 16
Single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
Two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
0 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
0 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
COMPUTER NETWORKS
Parity checking

## Slide 17
Sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment
COMPUTER NETWORKS
Internet checksum (review)

## Slide 18
More powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
Goal: choose r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G.
  If non-zero remainder: error
  detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern
COMPUTER NETWORKS
Cyclic Redundancy Check (CRC)

## Slide 19
We want:
  D.2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
or equivalently:
  D.2r = nG XOR R
or equivalently:
if we divide D.2r by G, want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1
COMPUTER NETWORKS
Cyclic Redundancy Check (CRC) : example

## Slide 20
nagasundaris@pes.edu
THANK YOU
S Nagasundari
Department of Computer Science and Engineering