## Slide 1
COMPUTER NETWORKS
S Nagasundari
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 3
COMPUTER NETWORKS
Multiple Access
Carrier Sense Multiple Access/Collision Detection
Class 48 : Multiple Access Protocols : Learning Objectives

## Slide 4
Two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP for dial-up access
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G. satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G
COMPUTER NETWORKS
Multiple access links protocols

## Slide 5
COMPUTER NETWORKS
Multiple access problem
How to coordinate the access of multiple sending and receiving nodes to a shared broadcast channel
Broadcast channels are often used in
  LANs,
  Networks that are geographically concentrated in a single building (or on a corporate or university campus).
Can I say Television as an example for Broadcasting??
  Traditional television-one-way broadcast
  While nodes on a computer network- broadcast channel can both send and receive

## Slide 6
COMPUTER NETWORKS
Human Protocols for sharing Broadcast channel
Give everyone a chance to speak.
Don’t speak until you are spoken to.
Don’t monopolize the conversation.
Raise your hand if you have a question.
Don’t interrupt when someone is speaking.
Don’t fall asleep when someone is talking

## Slide 7
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
Distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
Communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
Multiple access protocol
COMPUTER NETWORKS
Multiple access protocols
When multiple nodes are active in Broadcast channel,
coordinate the transmissions of the active nodes.

## Slide 8
Given: Multiple access channel (MAC) of rate R bps
Desirable characteristics:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. Fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple
COMPUTER NETWORKS
An ideal Multiple access protocol

## Slide 9
Three broad classes:
Channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
  Eg: TDM,FDM,CDMA
Random access
  channel not divided, allow collisions
  “recover” from collisions
  Eg. ALOHA,CSMA deployed in Ethernet
“Taking turns”
  nodes take turns, but nodes with more to send can take longer turns
COMPUTER NETWORKS
MAC protocols : Taxonomy

## Slide 10
Simple CSMA: listen before transmit:(Carrier Sensing)
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
Human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless
human analogy: the polite conversationalist
COMPUTER NETWORKS
CSMA ( Carrier Sense Multiple Access)

## Slide 11
Collisions can still occur with carrier sensing:
  Propagation delay means two nodes may not hear each other’s just-started transmission
Collision: entire packet transmission time wasted
  Distance & propagation delay play role in in determining collision probability
spatial layout of nodes
COMPUTER NETWORKS
CSMA : Collisions

## Slide 12
CSMA/CD reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes
COMPUTER NETWORKS
CSMA / CD

## Slide 13
NIC receives datagram from network layer, creates frame
If NIC senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame !
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval
COMPUTER NETWORKS
Ethernet CSMA / CD Algorithm

## Slide 14
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!
COMPUTER NETWORKS
CSMA / CD Efficiency

## Slide 15
nagasundaris@pes.edu
THANK YOU
S Nagasundari
Department of Computer Science and Engineering