## Slide 1
COMPUTER NETWORKS
S Nagasundari
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
Physical layer
Wireless LANs: IEEE 802.11
A day in the life of a web request

## Slide 3
COMPUTER NETWORKS
Synthesis of web request..
Class 56 : A day in the life of a web request : Learning Objectives

## Slide 4
Our journey down the protocol stack is now complete!
  application, transport, network, link
Putting-it-all-together: synthesis!
  Goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  Scenario: student attaches laptop to campus network, requests/receives www.google.com
COMPUTER NETWORKS
Synthesis : A day in the life of a web request

## Slide 5
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
Arriving mobile client attaches to network …
Requests web page: www.google.com
Scenario:
Sounds
simple!
COMPUTER NETWORKS
A day in the life of a web request

## Slide 6
router has
DHCP server
arriving mobile:
DHCP client
Connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
COMPUTER NETWORKS
A day in the life of a web request

## Slide 7
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
Encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
COMPUTER NETWORKS
A day in the life : Connecting to the Internet

## Slide 8
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
Before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
Client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply
COMPUTER NETWORKS
A day in the life…. ARP (Before DNS, Before HTTP)

## Slide 9
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
Demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
COMPUTER NETWORKS
A day in the life…. Using DNS

## Slide 10
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
To send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
Web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)
COMPUTER NETWORKS
A day in the life…. TCP Connection carrying HTTP

## Slide 11
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
Web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
COMPUTER NETWORKS
A day in the life…. HTTP Request / Reply

## Slide 12
Principles behind data link layer services:
  Error detection, correction
  Sharing a broadcast channel: multiple access
  Link layer addressing
Instantiation, implementation of various link layer technologies
  Ethernet
  switched LANS
Synthesis: a day in the life of a web request
Intro to Physical layer and Wireless LAN
COMPUTER NETWORKS
Summary

## Slide 13
Journey down protocol stack complete
Solid understanding of networking principles, practice!
….. could stop here …. but more interesting topics!
  deep understanding of wireless
  security
COMPUTER NETWORKS
Summary

## Slide 14
nagasundaris@pes.edu
THANK YOU
S Nagasundari
Department of Computer Science and Engineering