## Slide 1
COMPUTER NETWORKS
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Computer Networks and the Internet
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 3
COMPUTER NETWORKS
Network Core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 4
COMPUTER NETWORKS
Network Core: Packet Switching: store-and-forward
Transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
Store and forward: entire packet must arrive at router before it can be transmitted on next link
End-end delay: 2L/R (above), assuming zero propagation delay (more on delay shortly)
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 5
COMPUTER NETWORKS
Network Core: Packet Switching: queuing delay, loss
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for a period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link

## Slide 6
COMPUTER NETWORKS
Network Core: Two Key Network Core Functions
Forwarding:
local action: move arriving packets from router’s input link to appropriate router output link
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
Routing:
global action: determine source-destination paths taken by packets
routing algorithms
local forwarding table
local forwarding table
routing algorithm

## Slide 7
COMPUTER NETWORKS
Network Core: Circuit Switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 8
COMPUTER NETWORKS
Multiplexing in Circuit Switched Networks: FDM & TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
each call allocated its own band, can transmit at max rate of that narrow band
Time Division Multiplexing (TDM)
time divided into slots
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band, but only during its time slot(s)

## Slide 9
COMPUTER NETWORKS
Network Core: Packet Switching vs Circuit Switching
Example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
packet switching allows more users to use network!
N
users
1 Gbps link
…..
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
circuit-switching: 10 users
packet switching: with 35 users,
probability > 10 active users at same time is less than .0004 *
10 or few active users, probability 0.9996
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?

## Slide 10
COMPUTER NETWORKS
Network Core: Packet Switching vs Circuit Switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees traditionally used for audio/video applications
Is packet switching a “slam dunk winner”?
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet switching)?

## Slide 11
COMPUTER NETWORKS
Queries

## Slide 12
sivaramane@pes.edu
+91 80 6666 3333 Extn 834
THANK YOU
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering