## Slide 1
COMPUTER NETWORKS
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Computer Networks and the Internet
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 3
Performance: Delay, Loss & Throughput
COMPUTER NETWORKS
How do packet loss and delay occurs?
packets queue in router buffers
packets queue, wait for turn
arrival rate to link (temporarily) exceeds output link capacity: packet loss
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 4
Performance: Packet Delay – 4 Sources
COMPUTER NETWORKS
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 5
COMPUTER NETWORKS
Performance: Packet Delay – 4 Sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
* Check out the online interactive exercises: http://gaia.cs.umass.edu/kurose_ross

## Slide 6
Transmission Delay vs Propagation Delay
COMPUTER NETWORKS
Transmission Delay | Propagation Delay
Time required for the router to push out the packet. | Time it takes a bit to propagate from one router to the next.
A function of the packet’s length and the transmission rate of the link. | A function of the distance between the two routers.
dtrans = L/R | dprop = d/s
Nothing to do with the distance between the two routers. | Nothing to do with the packet’s length or the transmission rate of the link.

## Slide 7
Performance: Delay – Caravan Analogy
COMPUTER NETWORKS
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km

## Slide 8
COMPUTER NETWORKS
Performance: Delay – Caravan Analogy (more)
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 9
COMPUTER NETWORKS
Queries

## Slide 10
sivaramane@pes.edu
+91 80 6666 3333 Extn 834
THANK YOU
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering