## Slide 1
COMPUTER NETWORKS
Animesh Giri
Department of Computer Science & Engineering

## Slide 2
COMPUTER NETWORKS
Transport Layer
Animesh Giri
Department of Computer Science & Engineering

## Slide 3
COMPUTER NETWORKS
Connectionless Transport: UDP
Animesh Giri
Department of Computer Science & Engineering

## Slide 4: In this segment
COMPUTER NETWORKS
UDP: User Datagram Protocol [RFC 768]
UDP: segment header
UDP Checksum
  Internet Checksum: example
  Internet Checksum: weak protection!
Summary

## Slide 5
UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
COMPUTER NETWORKS
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control
  UDP can blast away as fast as desired
  can function in the face of congestion
why is there a UDP?

## Slide 6
UDP: User Datagram Protocol [RFC 768]
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
If reliable transfer needed over UDP:
  add needed reliability at application layer
  application-specific error recovery!
  add congestion control at application layer
COMPUTER NETWORKS

## Slide 7
UDP: User Datagram Protocol [RFC 768]
COMPUTER NETWORKS

## Slide 8
COMPUTER NETWORKS
SNMP server
SNMP client
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP: Transport Layer Actions

## Slide 9
COMPUTER NETWORKS
SNMP server
SNMP client
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP sender actions:
SNMP msg
is passed an application-layer message
determines UDP segment header fields values
creates UDP segment
passes segment to IP
UDPh
UDPh
SNMP msg
UDP: Transport Layer Actions

## Slide 10
UDP: Transport Layer Actions
COMPUTER NETWORKS
SNMP server
SNMP client
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP receiver actions:
SNMP msg
extracts application-layer message
checks UDP checksum header value
receives segment from IP
UDPh
SNMP msg
demultiplexes message up to application via socket

## Slide 11
UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
COMPUTER NETWORKS

## Slide 12
UDP Checksum
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
COMPUTER NETWORKS
Transmitted: 5 6 11
Received: 4 6 11
1st number
2nd number
sum
receiver-computed
checksum
sender-computed
checksum (as received)
=

## Slide 13
UDP Checksum
sender:
treat segment contents, including header fields, as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later …
Goal: detect “errors” (e.g., flipped bits) in transmitted segment
COMPUTER NETWORKS

## Slide 14
Internet Checksum: example
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
COMPUTER NETWORKS

## Slide 15
Internet Checksum: Weak protection!
COMPUTER NETWORKS
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!

## Slide 16
Summary
COMPUTER NETWORKS
“no frills” protocol:
  segments may be lost, delivered out of order
  best effort service: “send and hope for the best”
UDP has its plusses:
  no setup/handshaking needed (no RTT incurred)
  can function when network service is compromised
  helps with reliability (checksum)
build additional functionality on top of UDP in application layer (e.g., HTTP/3)

## Slide 17
animeshgiri@pes.edu
+91 80 6618 6603
THANK YOU
Animesh Giri
Department of Computer Science & Engineering