## Slide 1
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Find the range of addresses in the following blocks.
123.56.77.32/29
180.34.64.64/30
200.17.21.128/27

## Slide 2
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
You are given the network address 175.200.0.0; you are required to have 4 subnets.
What is the minimum number of Host Bits can you take in to the Network Bits for this purpose?
Write down the addresses of 4 subnets.
Write the subnet mask for the network.

## Slide 3
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
In a block of addresses, we know the IP address of one host is 25.34.12.56/16.
What are the first address (network address) and the last address (limited broadcast address) in this block?
Please explain in full with detailed steps showing the calculation.

## Slide 4
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
An organization is granted the block 16.0.0.0/8. The administrator wants to create 500 fixed- length subnets.
find the subnet mask
find the number of addresses in each subnet.
find the first and last address in first subnet and in the last subnet (500th subnet).

## Slide 5
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
An organization is granted a block of addresses with the beginning address 14.24.74.0/24. The organization needs to have 3 subblocks of addresses to use in its three subnets: one subblock of 10 addresses, one subblock of 60 addresses, and one subblock of 120 addresses. Design the subblocks.

## Slide 6
COMPUTER NETWORKS
IPv4 Addressing & Subnetting – Numerical Example
Find the network address and the directed broadcast address of subnetted Class B IPv4 address 172.25.171.182 with a subnet mask of 255.255.224.0.

## Slide 7
sivaramane@pes.edu
+91 80 6666 3333 Extn 834
THANK YOU
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering