## Slide 1
COMPUTER NETWORKS
S Nagasundari
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11

## Slide 3
COMPUTER NETWORKS
Physical Topology
Frame Structure
Class 50 : Ethernet : Learning Objectives

## Slide 4
“Dominant” wired LAN technology:
First widely used LAN technology
Simpler, cheap
Kept up with speed race: 10 Mbps – 400 Gbps
Single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
https://www.uspto.gov/learning-and-resources/journeys-innovation/audio-stories/defying-doubters
COMPUTER NETWORKS
Ethernet

## Slide 5
Bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
Switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
COMPUTER NETWORKS
Ethernet : Physical Topology
Traditional Ethernet
Nodes connected with coax
Long “runs” of wire everywhere
CSMA/CD protocol
Hub acts as a broadcast repeater Shorted cable “runs”, Useful for 100 Mbps – CSMA/CD protocol – Easy to add/remove users – Easy to localize faults – Cheap cabling (twisted pair, 10baseT)
Easy to increase data rate (e.g., Gbit Ethernet)
Nodes transmit when they want
Switch queues the packets and transmits to destination
Typical switch capacity of 20-40 ports
Each node can now transmit at the full rate of 10/100/Gbps
Modularity: Switches can be connected to each them using high rate ports

## Slide 6
Sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
Preamble:
Used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011
COMPUTER NETWORKS
Ethernet Frame Structure
Data:
46 to 1,500 bytes
Min-46

## Slide 7
dest.
address
source
address
data (payload)
CRC
preamble
type
Addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
Type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
COMPUTER NETWORKS
Ethernet Frame Structure ( more)

## Slide 8
Connectionless: no handshaking between sending and receiving NICs
Unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff
COMPUTER NETWORKS
Ethernet : Unreliable Connectionless

## Slide 9
  Different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
Many different Ethernet standards
  Common MAC protocol and frame format
  Different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
COMPUTER NETWORKS
802.3 Ethernet Standards: Link and Physical Layers

## Slide 10
COMPUTER NETWORKS
802.3 Ethernet Standards: Link and Physical Layers
Gigabit Ethernet is an extension of Ethernet standards
Data rate- 40,000 Mbps, 40 Gigabit Ethernet
Fully compatible with the huge installed base of Ethernet equipment.
Standard - IEEE 802.3z, does the following:
  Uses the standard Ethernet frame format
  Backward compatible with 10BASE-T and 100BASE-T technologies.
  Allows for point-to-point links as well as shared broadcast channels
    Point-to-point links use switches
    Broadcast channels use hubs
    Hubs-buffered distributors.
    Uses CSMA/CD for shared broadcast channels.
    In order to have acceptable efficiency, the maximum distance between nodes must be severely restricted.
    Allows full-duplex operation at 40 Gbps in both directions for point-to-point channels.

## Slide 11
nagasundaris@pes.edu
THANK YOU
S Nagasundari
Department of Computer Science and Engineering