## Slide 1
COMPUTER NETWORKS
S Nagasundari
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap
Introduction
Error detection, correction
Multiple access protocols
LANs
  Addressing, ARP
  Ethernet
  Switches
A day in the life of a web request
Physical layer
  Purpose, Signals to Packets
  Analog Vs Digital Signals
  Transmission Media
Wireless LANs: IEEE 802.11

## Slide 3
COMPUTER NETWORKS
Why, What- Wireless LAN
802.11 Architecture
Class 55 : IEEE 802.11- Wireless LAN : Learning Objectives

## Slide 4
COMPUTER NETWORKS
Wireless LAN
Network connectivity to the legacy wired LAN
Desktop
with PCI 802.11 LAN card
Laptop
with PCMCIA 802.11 LAN card
Provides network connectivity over wireless media
An Access Point (AP) is installed to act as Bridge between Wireless and Wired Network
The AP is connected to wired network and is equipped with antennae to provide wireless connectivity

## Slide 5
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 6
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure

## Slide 7
COMPUTER NETWORKS
IEEE 802.11- Wireless LAN
IEEE 802.11 defines
MAC protocol and
Physical medium specification
for wireless LANs

## Slide 8
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 9
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 10
COMPUTER NETWORKS
IEEE 802.11- Terminology

## Slide 11
COMPUTER NETWORKS
Characteristics of Selected Wireless Links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah
2 Key Areas:
Coverage area &
Link rate

## Slide 12
COMPUTER NETWORKS
Wireless Network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 13
COMPUTER NETWORKS
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: routing, address assignment, DNS-like name translation, and more.
Wireless Network

## Slide 14
COMPUTER NETWORKS
Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
infrastructure less
host connects to base station (WiFi, cellular) which connects to larger Internet. Eg: 4G LTE
no base station, no connection to larger Internet.
eg: Bluetooth, ad hoc nets
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other.
eg: MANET, VANET

## Slide 15
COMPUTER NETWORKS
IEEE 802.11 Wireless LAN (WiFi)
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions

## Slide 16
COMPUTER NETWORKS
The 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 17
COMPUTER NETWORKS
Basic Service Set
BSS- Smallest building block
  Number of stations
  Same MAC protocol
  Competing for access to same shared wireless medium
May be isolated or connect to backbone distribution system (DS) through access point (AP)
  AP functions as bridge

## Slide 18
COMPUTER NETWORKS
Extended Service Set
An Access Point (AP) broadcasts SSID (service set identifier) roughly every 100 ms and at 1 Mbps (to accommodate the slowest client)

## Slide 19
COMPUTER NETWORKS
802.11: Channels, Association
spectrum divided into channels at different frequencies
  AP assigns Service Set ID (SSID)
  AP admin chooses frequency for AP (2.4 GHz to 2.4835 GHz)
  interference possible: channel can be same as that chosen by neighboring AP! – WiFi Jungle
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication
  then typically run DHCP to get IP address in AP’s subnet
BSS

## Slide 20
COMPUTER NETWORKS
802.11 active/passive scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 21
COMPUTER NETWORKS

## Slide 22
nagasundaris@pes.edu
THANK YOU
S Nagasundari
Department of Computer Science and Engineering