## Slide 1
INTERNET OF THINGS
Connecting Smart Objects
Dr. Nagegowda K S
Department of Computer Science & Engineering

## Slide 2
INTERNET OF THINGS
Chapter4:Connecting Smart Objects
Dr. Nagegowda K S
Department of Computer Science & Engineering

## Slide 3
Agenda
INTERNET OF THINGS
Communication Criteria
IoT Access Technologies

## Slide 4
IoT Access Technologies
INTERNET OF THINGS
Standardization and alliances
Physical layer
MAC layer
Topology
Security
Competitive technologies

## Slide 5
IoT Access Technologies- IEEE 802.15.4
INTERNET OF THINGS
Home and building automation
Automotive networks
Industrial wireless sensor networks
Interactive toys and remote controls
ZigBee
6LoWPAN
ZigBee IP
ISA100.11a
WirelessHART
Thread

## Slide 6
IoT Access Technologies- ZigBee
INTERNET OF THINGS
Figure - High-Level ZigBee Protocol Stack

## Slide 7
IoT Access Technologies- ZigBee IP
INTERNET OF THINGS
Figure - ZigBee IP Protocol Stack

## Slide 8
IoT Access Technologies- Zigbee Physical Layer
INTERNET OF THINGS
2.4 GHz , 16 channels, with a data rate of 250kbps
915 MHz, 10 channels with a date rate of 40kbps
868 MHz, 1 channels with a date rate of 20kbps

## Slide 9
IoT Access Technologies- Zigbee Physical Layer
INTERNET OF THINGS
Figure - IEEE 802.15.4 PHY Format

## Slide 10
IoT Access Technologies- ZigBee MAC Layer
INTERNET OF THINGS
The 802.15.4 MAC layer performs the following tasks:
Network beaconing for devices acting as coordinators (New devices use beacons to join an 802.15.4 network)
PAN association and disassociation by a device
Device security
Reliable link communications between two peer MAC entities

## Slide 11
IoT Access Technologies- ZigBee MAC Layer
INTERNET OF THINGS
The MAC layer achieves these tasks by using various predefined frame types. In fact, four types of MAC frames are specified in 802.15.4:
Data frame: Handles all transfers of data
Beacon frame: Used in the transmission of beacons from a PAN coordinator
Acknowledgement frame: Confirms the successful reception of a frame
MAC command frame: Responsible for control communication between devices

## Slide 12
IoT Access Technologies- ZigBee MAC Layer
INTERNET OF THINGS
Figure - IEEE 802.15.4 MAC Format

## Slide 13
IoT Access Technologies- ZigBee Topology
INTERNET OF THINGS
Figure - 802.15.4 Sample Mesh Network Topology

## Slide 14
IoT Access Technologies- ZigBee Security
INTERNET OF THINGS
Figure - Frame Format with the Auxiliary Security Header Field for 802.15.4-2006 and Later Versions

## Slide 15
IoT Access Technologies- IEEE 802.15.4g and 802.15.4e
INTERNET OF THINGS
Distribution automation and industrial supervisory control and data acquisition (SCADA) environments for remote monitoring and control
Public lighting
Environmental wireless sensors in smart cities
Electrical vehicle charging stations
Smart parking meters
Microgrids
Renewable energy

## Slide 16
IoT Access Technologies- IEEE 802.15.4g and 802.15.4e
INTERNET OF THINGS
MAC Layer:
Time-Slotted Channel Hopping- TSCH
Information Elements
Enhanced beacons
Enhanced beacons requests
Enhanced Acknowledgement

## Slide 17
IoT Access Technologies- IEEE 802.15.4g and 802.15.4e
INTERNET OF THINGS
Figure - IEEE 802.15.4g/e MAC Frame Format

## Slide 18
IoT Access Technologies- IEEE 802.15.4g and 802.15.4e
INTERNET OF THINGS
Figure - IEEE 802.15.4g/e MAC Layer Security

## Slide 19
IoT Access Technologies- IEEE 1901.2a
INTERNET OF THINGS
Smart metering
Distribution automation
Public lighting
Electric vehicle charging stations
Microgrids
Renewable energy

## Slide 20
IoT Access Technologies- IEEE 1901.2a PHY
INTERNET OF THINGS
Figure - NB-PLC Frequency Bands

## Slide 21
IoT Access Technologies- IEEE 1901.2a MAC
INTERNET OF THINGS

## Slide 22
IoT Access Technologies- IEEE 1901.2a Topology
INTERNET OF THINGS

## Slide 23
IoT Access Technologies- IEEE 802.11ah
INTERNET OF THINGS
Sensors and meters covering a smart grid
Backhaul aggregation of industrial sensors and meter data
Extended range Wi-Fi

## Slide 24
IoT Access Technologies- IEEE 802.11ah MAC
INTERNET OF THINGS
Number of devices
MAC header
Null data packet support
Grouping and sectorization
Restricted access window
Target wake time
Speed frame exchange

## Slide 25
IoT Access Technologies- IEEE 802.11ah Topology
INTERNET OF THINGS

## Slide 26
nagegowda@pes.edu
THANK YOU
Dr. Nagegowda K S
Department of Computer Science & Engineering